## Slide 1: Integrated Visual Field Testing and Remapping for Hemianopia using Virtual Reality
by Nik Harith Sharifuddin (2673209B)

## Slide 2: Outline
Introduction, motivations & aims
Design
Implementation
User Evaluation
Results & Discussion
Conclusion

## Slide 3: Introduction

## Slide 4
Introduction
Hemianopia is a cortical visual impairment that limits the visual field of a person to half of it, either to the right or left side
Commonly caused by stroke, it reduces spatial awareness, making tasks such as navigation, reading and driving difficult.
Motivations:
The devices used to assess hemianopia are often expensive and requires an expert.
Common ways alleviate the effects of hemianopia uses methods such as Fresnel glasses are often ineffective in improving the condition in the long run.
Virtual Reality (VR) technology, packed with numerous features such as eye-tracking and camera passthrough has become more accessible and have the potential to be utilised to help people with hemianopia.

## Slide 5: Outline
Aims:
This project continues the efforts of previous students developing the various ways to detect the visual impairment, specifically hemianopia, and aid people that has it using VR technology.
Those projects however were developed separately and are disjoint from each other at the moment.
There is a need to integrate them into a single application so that functionalities could be combined and complement each other’s functionalities.
The application would also be extensible, and new features may be added easily.
This is a collaboration project, where I mostly focused on the integration part and Visual Field Remapping (VFR), while Caleb, worked on the Visual Field Testing (VFT) module.

## Slide 6: Design

## Slide 7
State
Process/ interaction
A common menu (CORE menu) encompasses both modules we want to integrate.
Both modules retains their functionalities from previous projects.
Users can access both modules without leaving the application.
Application workflow

## Slide 8
Sample of common user interface to be used in the final application
Used across all menu in the application
Common user interface

## Slide 9
A new feature implemented to improvise the process of remapping the live camera feed
Intended to reduce cybersickness and increase accuracy and efficiency
Automatic remapping
Preset position & scale
Increment/decrement position & scaling gradually
Stops adjustments
Continue to adjust position & scaling
while position <=preset
when preset position/scaling achieved

## Slide 10: Implementation

## Slide 11
Hardware
Software
Software we used:
Unity v2019.4.35f1
SteamVR
SRWorks SDK
SRAnipal
Unity scripting was done in C#
Parts of the VFT module uses Python for eye tracking data processing and reporting
HTC Vive Pro Eye headset
PC workstation:
  Intel Core i9-12900K, 3.2GHz
  64GB of RAM
  NVIDIA GeForce RTX 3080 Ti

## Slide 12
Application now integrates both VF Testing and Remapping modules
Common user interface developed with consistent themes and colours across all menus

## Slide 13
Automatic remapping was achieved by using presets to transform the position and scale of the live camera passthrough
We defined presets of position and location for certain hemianopia conditions;
  Homonymous hemianopia, Right
  Homonymous hemianopia, Left
  Quadrantanopia, Right Temporal
  Quadrantanopia, Left Parietal

## Slide 14: Application Demo

## Slide 15
VF Testing Demo
<Application demo not included>

## Slide 16
VF Remapping Demo
<Application demo not included>

## Slide 17: Evaluation & Results

## Slide 18
The evaluation chose to focus on analysing the effectiveness of automatic remapping, while also assessing the usability of the application.
Participants were simulated with partial blindness and were asked to identify some objects on a table in camera passthrough mode.
Then, they would try to remap their blocked vision in manual mode, or they would select the automatic remap option so they could see all objects on the table.
We assessed 4 conditions:
  Homonymous hemianopia, Right
  Homonymous hemianopia, Left
  Quadrantanopia, Right Temporal
  Quadrantanopia, Left Parietal
A survey consisting of SSQ and NASA-TLX questionnaires were filled in after each conditions

## Slide 19
Hypothesis:
“Automatic remapping results in better efficiency, accuracy and comfort compared to manual remapping”
Efficiency: measured by time taken to remap in each of the two modes.
Accuracy: measured by difference between the final remapped position and scaling of the live camera passthrough between both modes.
Comfort: measured by SSQ and NASA-TLX scores, with lower the scores indicate better results.

## Slide 20
Mean time taken to remap shows that automatic remapping outperforms manual remapping, mainly due to its fixed preset nature.
In both modes, quadrantanopia conditions takes longer to remap. This may be caused by the asymmetrical shape of the simulated blindness required the user to spend more time finding the right position/scaling.
Results: Mean time taken to remap

## Slide 21
Results: Mean remapped X-axis position
Mean final remapped position (taken with X-axis) reveals that there are little differences between both remapping modes for homonymous hemianopia conditions, supporting our hypothesis.
Quadrantanopia conditions have big differences (~ ± 0.5) between the two modes, suggesting unsuitability of the preset settings.

## Slide 22
Mean final remapped scale (uniform on X & Y axis) reveals the inverse of the previous remapped final position results.
Here, the differences between both remapping modes for quadrantanopia conditions are miniscule, supporting our hypothesis.
Homonymous hemianopia conditions this time have differences around 0.10 between the two modes, suggesting the preset settings needs more improvement to adapt to these conditions.
Results: Mean final remapped scale

## Slide 23
There are less instances of simulator sickness reported after the automatic remapping was performed compared to manual remapping mode.
Possibly due to the simpler process of automatic remapping requiring participants to exert less effort to complete the task.
Results: SSQ

## Slide 24
The mean task load for both remapping modes are not that different, meaning the perceived workload for both modes are the same.
This suggests that participants experienced the same amount of perceived comfort between both modes.
Results: NASA-TLX

## Slide 25
Half of the participants (n=8) prefers automatic remapping while the other half prefers manual remapping, a perfect half split.
Participants felt the program was user friendly and intuitive. They also felt it would be useful for people with visual impairment.
Some participants felt there are still works to be done to improve the user interface, citing the need to adapt to the general public especially people with visual impairment.
Results: General Usability

## Slide 26: Limitations
Sample size is only (n=8) participants, limiting the validity and generalisability of the results experiment.
Some parts of the experiment were difficult to control despite best efforts made to control them, such as the viewing angle of the participant while seated during the experiment due to different heights of the participant.

## Slide 27: Conclusion

## Slide 28
Conclusion
This project achieved the goal to integrate both of the Visual Field Testing and Remapping modules into one single VR application.
This will simplify and streamline the process of adding new feature in future development.
A new feature to improve the comfort of remapping the visual field was also developed.
Results from user evaluation reveals that it is more efficient in terms of the time needed to do the remapping process
However, further improvements are needed for the automatic remapping to be fully useful for those with Hemianopia.

## Slide 29
Future works
Automatic remapping with VFT Data
  Personalised remapping procedure, rather than preset.
Porting to the latest version of Unity
  Use the latest version to access latest features and conform to latest standards
Portability of HMD
  Use newer and lighter HMDs for the application, increasing comfort.
Adaptive remapping
  Use eye-tracker to responsively adjust the remapped vision to where the user is seeing, rather than static

## Slide 30: Questions?

## Slide 31: Thank you! I enjoyed working on this project and putting my effort into it.  Nik Harith 2673209B